## Slide 1: Brain tumor segmentation using deep learning
Roy Hirsch, Ori Chayoot
Pro-2018-049
Advisor: Dr. Tammy Riklin-Raviv

## Slide 2: Introduction:
Galioma brain tumor is the most frequent primary brain tumors in adults
MR imaging is used for prediction and evolution of tumors before and during treatment
The tumors are diverse in terms of size, shape, extension and localization
Project’s goal:
Accurate semantic segmentation of different tumor regions from multi-modal MRI scans using deep neural networks.
Notes: Galiomas represent 24.7% of all primary brain tumors and 74.6% of all malignant tumors.
There are more than 100 histologically distinct types of primary brain and central nervous system tumors.
Because of their unpredictable appearance and shape, segmenting brain tumors from multi-modal imaging data is one of the most challenging tasks in medical image analysis.

## Slide 3: Project’s timeline:
Aug-Sep 17’:
Independent studies of DNN course
Oct 17’:
Literature review
Dec 17’ -Feb 18’:
Implementation of classical segmentation algorithm
Nov-Dec 17’:
Independent studies of TF.
Start building NN framework
Feb 18’:
Implementation of basic Unet NN for toy data
Mar 18’:
Implementation of Unet NN for BRATS data

## Slide 4: Dataset:
BRATS dataset (2012):
Global challenge for brain tumor segmentation
20 HGG and 10 LGG MR multimodal images (T1, T2, T1g, FLAIR)
The images are co-registered and skull stripped
HG-001, slice: 80
Notes: Post-Gadolinium T1 scan:
Gadolinium (Gd) is a metallic element (atomic number 64) that can be chelated into paramagnetic agents that are injected intravenously during MR imaging.
The gadolinium ion is useful as an MRI agent because it has seven unpaired electrons, which is the greatest number of unpaired electron spins possible for an atom.
Gd molecules shorten spin-lattice relaxation time (T1) of voxels in which they are present.
As a result, on T1-weighted images they have a brighter signal. This can have a number of utilities:
Detection of focal lesions, e.g. tumour, abscess, metastasis
imaging of vessels in MR angiography
characterization of liver lesions, based on enhancement characteristics, e.g. hepatoma and haemangioma
Blood vessels and pathologies with high vascularity appear bright on T1 weighted post gadolinium images.
Gadolinium contrast agents are the most commonly used for enhancement of vessels in MR angiography or for brain tumor enhancement associated with the degradation of the blood–brain barrier. One GD atom can relax million water molecules in a second. GD is a paramagnetic material
Flair scan:
FLAIR: fluid-attenuated inversion-recovery MRI: bright signal of the CSF (cerebrospinal fluid) is suppressed which allows a better detection of small hyperintense lesions.
In FLAIR, the signal from fluid is nullified by using a long effective echo time and long inversion time. Inversion recovery sequence with a long inversion time (TI) of 2000-2500 is used for fluid suppression. This sequence is commonly used in the brain and spinal cord where the lesions are normally covered by bright cerebrospinal fluid (CSF) signals. A long inversion time suppresses the high CSF signal and improve the visualization of small periventricular and spinal cord lesions.

## Slide 5: Dataset:
BRATS dataset (2012):
Ground true manual segmentation:
  (0) Background
  (1 - green) Necrotic center and fluid collections
  (2 - yellow) Edema
  (3 - brown) Non-enhancing tumor
  (4 - blue) Enhancing tumor
Measure metrics:

## Slide 6: Classical segmentation algorithm:
Auto-thresholding of T2 and FLAIR scans.
Otsu’s method
Active contour for optimized segmentation
Chan and Vese level-set
Morphological operations
Deleting small connected components, gaps filling
Pre-processing
Contrast enhancement
Notes: Different separtion stages per modality

## Slide 7: Classical segmentation algorithm:
Auto-thresholding of T2 and FLAIR scans.
Otsu’s method
Active contour for optimized segmentation
Chan and Vese level-set
Morphological operations
Deleting small connected components, gaps filling
Pre-processing
Contrast enhancement
Otsu’s method: clustering method, based on finding the thresholds that minimize the intra-class variance of the image histogram.
Dice Score = 0.74
Sensitivity=0.61
Specificty=0.9994
AND
Notes: Different separtion stages per modality

## Slide 8
Otsu’s Method –T2 results
Notes: מציגים את החלוקה של הבינים , להראות שקיימים ווקסלים אשר שייכים לגידול אך השיטה לא זיהתה (בגלל הווריאנס הרחב ומספר הפיקסלים הקטן יחסית?).
לציין שבסף הנמוך קיימת דלתה של אפסים שלא מוצגת בהיסטוגרמה

## Slide 9
Otsu’s Method –Flair results
Notes: לציין שכאן קיימת הפרדה טובה יותר בין הווקסלים של הגידול לווקסלים שאינם שייכים לגידול

## Slide 10: Classical segmentation algorithm:
Auto-thresholding of T2 and FLAIR scans.
Otsu’s method
Active contour for optimized segmentation
Chan and Vese level-set
Morphological operations
Deleting small connected components, gaps filling
Pre-processing
Contrast enhancement
Auto-threshold mask:
Cleaned mask:
Notes: Different separtion stages per modality

## Slide 11: Classical segmentation algorithm:
Auto-thresholding of T2 and FLAIR scans.
Otsu’s method
Active contour for optimized segmentation
Chan and Vese level-set
Morphological operations
Deleting small connected components, gaps filling
Pre-processing
Contrast enhancement
Chan Vese Level-set:
Iterative contour optimization by
minimalizing the following cost function:
Active Contours Without Edges , Chan and Vese, IEEE, 2001
Notes: Different separtion stages per modality

## Slide 12
Dice = 86.43
Dice = 91.83
Final Results:
Dice=0.7854
Dice=0.8416
Notes: השינוי נתן עליהה ממוצעת של 4 אחוז בין התמונות ואצל רוב התמונות אכן היה שיפור.

## Slide 13
Level set parameters:
Smoothness factor = 1.2
Iterations number = 5
Final Results:
AVG | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | score
76 | 84 | 74 | 93 | 74 | 88 | 89 | 82 | 46 | 59 | 91 | 5 | 83 | 83 | 68 | 92 | 66 | 92 | 86 | 88 | 82 | Dice %
75 | 88 | 63 | 92 | 94 | 90 | 91 | 70 | 57 | 54 | 94 | 2 | 79 | 85 | 70 | 94 | 51 | 86 | 87 | 91 | 77 | Sens %
0.997 | 0.994 | 0.999 | 0.999 | 0.994 | 0.998 | 0.995 | 0.999 | 0.998 | 0.999 | 0.997 | 1.0 | 0.996 | 0.994 | 0.997 | 0.998 | 0.999 | 0.999 | 0.996 | 0.998 | 0.993 | Spec
Notes: בחרנו בגישה קצת נאיבית שמניחה חוסר תלות בין הפרמטרים למרות שזה לא נכון ולקחנו את הערכים שהביאו למקסימום בכל סריקת פרמטר כלשהו. באופן מפתיע זה עבד ושיפרנו ב5 אחוזים את הריצה המקורית (עם אלפא 2 , דלתא טי 4 ומקדם חלקות של 1)שלנו עבור 20 דוגמאות
סטיית תקן של 0.2 צריך להוסיף.

## Slide 14
U-Net: Convolutional Networks for Biomedical Image Segmentation
Olaf Ronneberger et al, International Conference on Medical Image Computing and Computer-Assisted Intervention, 2015
Unet neural network architecture:
State-of-the-art architecture for semantic segmentation of bio-medical data.
Deep feature extraction, up sampling with residual connections
Notes: בחרנו בגישה קצת נאיבית שמניחה חוסר תלות בין הפרמטרים למרות שזה לא נכון ולקחנו את הערכים שהביאו למקסימום בכל סריקת פרמטר כלשהו. באופן מפתיע זה עבד ושיפרנו ב5 אחוזים את הריצה המקורית (עם אלפא 2 , דלתא טי 4 ומקדם חלקות של 1)שלנו עבור 20 דוגמאות
סטיית תקן של 0.2 צריך להוסיף.

## Slide 15
Unet neural network architecture:
Insert here results of toy data and BRATS data
Notes: בחרנו בגישה קצת נאיבית שמניחה חוסר תלות בין הפרמטרים למרות שזה לא נכון ולקחנו את הערכים שהביאו למקסימום בכל סריקת פרמטר כלשהו. באופן מפתיע זה עבד ושיפרנו ב5 אחוזים את הריצה המקורית (עם אלפא 2 , דלתא טי 4 ומקדם חלקות של 1)שלנו עבור 20 דוגמאות
סטיית תקן של 0.2 צריך להוסיף.

## Slide 16
Future work:
Deeper literature review for different network architectures.
Implementation of more complex, accurate and innovative architecture:
  3D Unet
  FCN+LSTM
  More…
Notes: בחרנו בגישה קצת נאיבית שמניחה חוסר תלות בין הפרמטרים למרות שזה לא נכון ולקחנו את הערכים שהביאו למקסימום בכל סריקת פרמטר כלשהו. באופן מפתיע זה עבד ושיפרנו ב5 אחוזים את הריצה המקורית (עם אלפא 2 , דלתא טי 4 ומקדם חלקות של 1)שלנו עבור 20 דוגמאות
סטיית תקן של 0.2 צריך להוסיף.